|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Band saw |
| Dangers for humans and the environment |
|  | Tilting workpieces can tear the band saw blade and cause serious injury. Contact with the band saw blade causes cuts.. In case of strong noise (from 80 dB (A)) there is a risk of hearing damage. The running band saw blade can grasp and pull in the work clothes. Chips and sharp-edged components may cause cuts. Danger of accident due to damaged band saw blades (for example blunt, torn). There is a risk of skin diseases when working with cooling lubricants. |
| Protective measures and rules of conduct |
|  | The operating instructions of the manufacturer must be observed! Avoid tilting the workpiece when the workpiece is fed to the band saw blade. Dress band saw blade to the part required for cutting. Contact with the band saw blade must be avoided. Use personal protective equipment (including skin protection). Wear tight-fitting work clothes. Switch off the machine even during short interruptions and cover the saw blade behind. Do not remove splinters, chips and waste by hand, but with suitable tools. Do not use damaged band saw blades. It is forbidden to wear protective gloves (danger of getting into the rotating blade). To wear ear protection. If there is a risk of eye injuries, the goggles must be worn. Switch off the machine even during short interruptions and cover the saw blade behind. | pE |
| Faults and dangers |
|  | • If work equipment fails, discontinue work and inform the responsible teacher. |  |
| Accidents and First Aid |
|  | Attract first responders Emergency call: 144 Report accident to responsible |  |
| Tests – Maintenance - Disposal |
| Maintenance (maintenance, repair) should only be carried out by qualified and authorized persons. After maintenance, the protective equipment must be checked. Observe the operating instructions of the manufacturer during maintenance. Regular checks (e.g., electrical, mechanical) by qualified persons. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |