|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Compressed gas cylinders |
| Dangers for humans and the environment |
|  | Risk of injury when falling over. Release the stored pressure energy by mechanical damage u. unintentional opening of the valve. Explosion of gas bottles in case of excessive heating. Health and fire hazard due to release of gases due to leaking gas connections. Uncontrollable reactions of the contents gases due to the ingress of air or oil (oxygen) due to the backflow of gaseous u. liquid foreign substances e.g. from other gas bottles. |
| Protective measures and rules of conduct |
|  | Do not carry or roll gas bottles, but transport them with a bottle cart. Only transport with protective cap. Wear protective shoes and protective gloves Secure against falling over (chaining). Put on protective cap. Open the gas cylinder valves slowly to avoid pressure surges. Close valves at the end of work. Empty gas cylinders only to a residual pressure (approx. 1.5 bar). Do not touch the gas cylinders with the flame, do not oil or grease, do not force open. protection of gas cylinders against fire hazard, e.g. Do not store together with flammable liquids. Keep away from sources of ignition and heat. | pE |
| Faults and dangers |
|  | In the event of damage to the gas cylinders or the valves: close the valves and inform the workshop management. In case of damage to the protective equipment or other faults, inform the workshop management. Have damage repaired by qualified personnel only. |  |
| Accidents and First Aid |
|  | Close the gas cylinder. Close valves. Inform first responders (see alarm plan). Provide minor injuries immediately. make an entry in the association book. In the case of major injuries, consult a general practitioner (see "First Aid") or call the emergency medical service via Tel.144 Inform the workshop management .. |  |
| Tests – Maintenance - Disposal |
| Defects on the gas cylinder / on the fittings must be reported to the workshop management immediately. Repair only by instructed and instructed persons |
| Signatures |
| Supervisor: Signature: Town: Date: |  |