|  | Operating instructions |  |
| --- | --- | --- |
| Equipment - Apparatus - Device |
| Double - grinders |
| Dangers of environment |
|  | Workpieces may heat up during processing - danger of burns Injuries due to abrasive disc breakage or defective abrasive belt Eye injuries from worn materials Foot injuries caused by falling workpieces Hand injuries due to sharp-edged surfaces Hearing damage due to noise Machine caster Collection of clothing and / or hair, gloves flying sparks, danger of fire Health hazard due to the formation of dusts (see material properties) |
| Protective measures and rules of conduct |
|  | The operating instructions of the manufacturer must be observed! Wear protective goggles and shoes suitable for the area Depending on the materials and activities, additional dust mask and ear protection must be worn The clamping of a suitable grinding wheel / belt may only be carried out by instructed employees. After each new clamping a test run of ~ 20 minutes is to be carried out. Workpiece supports and protective covers must be adjusted regularly. The distance between the grinding wheel / sanding belt and the workpiece support must not exceed 3 mm, between the grinding wheel and the sanding hood at most 5 mm. If necessary, wear only suitable gloves. Wear tight fitting clothes Wear hairnet for long hair Take fire protection precautions. For example, remove flammable substances / materials | pE |
| Disruptions and dangers |
|  | In case of malfunction or damage to machinery or protective equipment Switch off the machine and secure against unauthorized restarting Have damage repaired by qualified personnel only |  |
| Accidents and first aid |
|  | Keep Calm observe self-protection; Injured people recover, switch off the system Call first responder and, if necessary, emergency doctor. Emergency call: 144 provide first aid Inform supervisors An accident report must be made in the case of accidents and near-misses. |  |
| Tests - Maintenance - Disposal |
| Repair only by authorized and qualified persons For setup, maintenance and care work, disconnect or secure the machine from the mains After maintenance, the protective equipment must be checked. E-check, depending on the model, annually or every four years by a trained electrician (stationary or mobile machine) |
| Signatures |
| Supervisor: Signature: Town: Date: |  |
| Signatures |  |