|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Drying Ovens |
| Dangers for humans and the environment |
|  | There are hazards due to: Risk of burns from fingers and hands on hot surfaces. Danger of crushing the fingers when pushing in the hordes or when closing the door. Irritation of the respiratory tract due to dust formation, especially with dried material. Irritation of the respiratory tract due to substances contained in the product, e.g. Solvent. Possibly. Irritation of the skin in direct skin contact with the dry matter. Risk of explosion in the presence of flammable solvents Risk of fire in combustible dry matter due to spontaneous combustion Slipping hazard due to spilled product. |
| Protective measures and rules of conduct |
|  | The employees must be instructed in the handling of the drying oven. Wear mandatory PPE (basis: risk assessment). Take care when handling the substances to be dried, if necessary observe BA hazardous substances. Pick up spilled product immediately and dispose of according to the operating instructions. Clean and care for hands after contact with the product (see skin protection plan). Extract exhaust air from the drying oven as far as possible to the outside, if necessary clean it with an exhaust air scrubber. Always close the drying oven well. For drying with flammable solvents, use only Ex-protected technical equipment. Observe Ex protection guidelines. | pE |
| Faults and dangers |
|  | Do not use the drying oven in case of defective or faulty extraction. Only rectify faults in the electrical heating by qualified electricians. Do not use the drying oven in case of defective or faulty extraction. Only rectify faults in the electrical heating by qualified electricians. |  |
| Accidents and First Aid |
|  | In case of skin contact with the product to be dried, rinse with plenty of water, consult a doctor if necessary. Injured skin increases the health risk significantly. Depending on the type of injury, provide first aid as far as possible, call for help if necessary. Instruct assistants and point out special dangers. Emergency call: 144 |  |
| Tests – Maintenance - Disposal |
| Regularly check drying oven for proper condition (see manufacturer's recommendation). Dispose of drying cabinets only after sufficient cleaning in accordance with legal regulations (electronic waste). |
| Signatures |
| Supervisor: Signature: Town: Date: |  |