|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Edge Bank |
| Dangers for humans and the environment |
|  | Risk of severe cuts due to sharp edged metal sheets Bruising by moving up and down the bending beam or through the upper beam Jumping out of improperly clamped workpieces Clamping clothes when clamping workpieces |
| Protective measures and rules of conduct |
|  | The operating instructions of the manufacturer must be observed! Never override safety devices (for example, to clear jammed workpieces) Do not exceed the prescribed thicknesses or bending radii Keep the workplace clean and tidy. Store workpieces to be machined only in the immediately required quantity in the work area Pay attention to the distance of the hands when setting the workpieces Stepping out of the swivel range of the bending beam Wear tight fitting clothes Scarves, watches, hand and arm jewelery are not allowed wear gloves (against cuts) Working with two people only after consultation with the responsible person Do not put your hands in the danger area | pE |
| Faults and dangers |
|  | Secure the device in the event of damage to the device or its protective equipment Have damage repaired by qualified personnel only |  |
| Accidents and First Aid |
|  | secure the device Inform first responders Provide immediate injury Emergency call: 1 |  |
| Tests – Maintenance - Disposal |
| Repair only by authorized and qualified persons After maintenance, the protective equipment must be checked. Clean the machine after work |
| Signatures |
| Supervisor: Signature: Town: Date: |  |