|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Electric welding WIG |
| Dangers for humans and the environment |
|  | Increased electrical hazard inhalation of welding fumes Dangers to eyes and skin due to UV rays Danger due to hot surfaces |
| Protective measures and rules of conduct |
|  | Check the device and the cable for defects before use (also on the validity of the test stickers). Switch on the suction device before starting work and adapt it to workpieces Protect cables against damage. Wear personal protective equipment and ensure a safe condition: Perform skin protection according to skin protection plan, Wear welding gloves with cuffs (without metal rivets), Wear a face shield or protective hood with a matched protective filter Wear tight fitting fire-resistant work clothing Make sure that welding assistants wear personal protective equipment. Take anti-glare measures for others (eg close the curtain) Only use welding and soldering equipment after instruction Secure or remove combustible materials Make good conductivity between earth cable and workpiece: If possible on the workpiece or at a small distance and firm connection. | pE |
| Faults and dangers |
|  | In case of fire, carry out a fire test |  |
| Accidents and First Aid |
|  | Keep Calm Involve first responders Emergency call: 144 interrupt the power supply Provide immediate injury |  |
| Tests – Maintenance - Disposal |
| Repair only by instructed and instructed persons Clean workplace after work Annual e-check by authorized electrician (mobile) |
| Signatures |
| Supervisor: Signature: Town: Date: |  |