|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Electric welding |
| Dangers for humans and the environment |
|  | Infrared or ultraviolet radiation (arc), flare of the eyes Flying sparks, danger of fire, burning of the skin Electric shock Welding of containers: Danger due to residues of the ingredients! Welding fumes: health hazard during welding work on high-alloyed workpieces, metallic coatings, paint coatings, plastic coatings, contamination by oils, greases or residual solvents etc. |
| Protective measures and rules of conduct |
|  | For welding work in areas with a fire and explosion hazard, obtain a welding permit Remove or cover combustible parts from the environment Provide fire extinguishers Check the welding generator, cable, electrode holder and ground terminal for defects before use Establish good conductivity between earth cable and workpiece Switch on the suction device before starting work and adjust if necessary Always place the burner in an insulated position (if possible, remove the electrode residue) Protect cables against damage, use cables with insulated couplings Do not clamp the welding wire holder and inert gas welding torch under the arm and place it only on insulating shelves Position protective gas bottle securely and secure against falling over Observe the operating instructions "Electrical welding under increased electrical hazard" when welding under increased electrical hazard When welding containers with flammable liquids, empty container completely and fill with water Use protective shield or protective shield with welding protection filter, wear sweat-proof gloves and clothing, also for welding assistants Switch off the welding machine before connecting the welding cables After completing the welding work, ensure a fire station | pE |
| Faults and dangers |
|  | In case of defects, do not use the device and inform the supervisor If the extraction system fails, discontinue work and inform supervisors |  |
| Accidents and First Aid |
|  | Keep Calm Involve first responders Emergency call: 144 To report an accident In the event of a power accident: Disconnect the power and remove the injured from the circuit In case of respiratory or cardiac arrest initiate resuscitation and alert the emergency physician |  |
| Tests – Maintenance - Disposal |
| Performing maintenance work only by authorized specialist personnel Replace damaged insulating jaws and welding wire holder immediately Change the wire reels only when they are de-energized |
| Signatures |
| Supervisor: Signature: Town: Date: |  |