|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Gas welding |
| Dangers for humans and the environment |
|  | Fire and explosion hazard inhalation of welding fumes Dangers to eyes and skin due to UV rays Danger due to hot surfaces |
| Protective measures and rules of conduct |
|  | Check the device and hoses for defects before use (also valid for the inspection labels). Switch on the suction device before starting work and adjust it if necessary Protect hoses from damage and prevent standing gas cylinders from falling over Wear personal protective equipment and ensure a safe condition: Apply skin protection according to skin protection plan Wear welding gloves with cuffs (without metal rivets), Wear protective goggles with a matched protective filter Wear protective sleeves, gaiters, aprons made of flame retardant material or a welder protective suit. Wear appropriate safety shoes in the area Make sure that welding assistants wear personal protective equipment Take anti-glare measures for others (eg close the curtain) Close taps before coupling the welding hoses and at the end of the work. Only use welding and soldering equipment after instruction Only transport gas bottles with the protective cap screwed on When starting up, first open the oxygen valve slightly. Secure or remove combustible materials When finishing work, first close the burner valve Do not bring oxygen bottles and their fittings into contact with oil or grease At the end, bend the welding rods due to risk of injury. Pay attention to further fire and explosion hazards Mehr anzeigenWeniger anzeigen | pE |
| Faults and dangers |
|  | Defects on the gas bottles and hoses must be reported immediately In case of fire, carry out a fire test |  |
| Accidents and First Aid |
|  | The (first responder informing) Provide immediate injury Emergency call: 144 |  |
| Tests – Maintenance - Disposal |
| Only repaired by instructed and instructed persons Clean workplace after work Regular inspection of gas cylinders and hoses |
| Signatures |
| Supervisor: Signature: Town: Date: |  |