|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Grinding machine |
| Dangers for humans and the environment |
|  | Cutting injuries on the workpiece Abrasive damage to abrasive belt and grinding wheel Fast rotating grinding wheel / belt, trailing grinding wheel / belt Breakage of the grinding wheel, tearing of the grinding belt Injuries due to flying workpiece or tool parts Flying sparks and fire Noise development and dust generation Risk of entanglement Risk of burns on heated workpiecesMehr anzeigen Weniger anzeigen |
| Protective measures and rules of conduct |
|  | Operation of the machine only after instruction. Wear tight-fitting work clothing, safety shoes, ear protection and safety goggles! For long hair wear a hairnet or a suitable cap! Wearing jewelery (rings, chains, watches, visible piercings) is prohibited. The wearing of gloves is prohibited. Removing fire loads in the workplace. Before clamping a grinding wheel Crack test by sound sample. Clamping a new grinding wheel only by instructed persons. After clamping test run of 20 minutes. Watch the tape run and center or tension if necessary. Check machine for obvious damage. Workpiece supports and protective covers must be readjusted regularly. Distance between workpiece support and grinding wheel max. 3 mm. Attention to follow-up of the machine after switching off! | pE |
| Faults and dangers |
|  | In the event of faults, abnormalities of the machine, breakage and setting of tools, switch off the machine immediately, secure it against commissioning and inform the supervisor. Only eliminate faults when the machine is at a standstill. |  |
| Accidents and First Aid |
|  | Keep Calm Observe self-protection; Injured people recover, switch off the system Call first responder and, if necessary, emergency doctor. Emergency call: 144 Provide first aid Inform supervisors An accident report must be made in the case of accidents and near-misses. |  |
| Tests – Maintenance - Disposal |
| The machine and the workplace are to be cleaned after use, tools and aids are to be put in the designated places. Replace damaged grinding wheels and abrasive belts immediately. Repair and repair only by authorized and authorized persons. Observe the maintenance schedule of the manufacturer. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |