|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Laminar Flow |
| Dangers for humans and the environment |
|  | Danger due to UV lamp (ozone formation) danger by gas flame (combustion) |
| Protective measures and rules of conduct |
|  | Each use of the laminar flow should be entered in the log book, it should be noted whether with or without Bunsen burner (gas) was worked. Switch on the UV light for approx. 5 minutes before use. Do not expose hands and eyes directly to UV light. Start the laminar flow by o Opening the sliding glass window (up to the black dot); Acoustic signal sounds Switch on fan. Acoustic signal goes out, the laminar flow lights go out, the device is in the warm-up phase (about 3 minutes). After warming up, the lights come on, the unit is ready for use If Bunsen burner is used, proceed as follows: In the control bar, switch on the button with 'socket symbol' (socket), click sound is noticeable. Turn gas area under tables (2 turns) Turn right outside of the laminar flow yellow rotary valve (2 turns) Turn the rotary valve on the bottom left of the Bunsen burner and press on the locking pin, hold it with the lighter during the manual ignition, then release it. Check that the flame has a bluish color and max. 5-6 cm high. If necessary regulate via the air supply (rotary knob). Switching off the Bunsen burner: Close the gas bottle, the flame goes out, close the yellow rotary valve after approx. 10 sec., Then close the rotary valve on the Bunsen burner | pE |
| Faults and dangers |
|  | Close the valve on the gas cylinder immediately in the event of an alarm. Repair and repair must be carried out exclusively by a specialist workshop. |  |
| Accidents and First Aid |
|  | In the event of burns, alert first aiders, rescue service or doctor if necessary. Inform supervisor (if necessary entry in the association book). |  |
| Tests – Maintenance - Disposal |
| Maintenance and repair work may only be carried out with the written permission of the laboratory manager. Only spare parts that have the same material and design as the original parts may be used for maintenance. Observe the maintenance schedule of the manufacturer. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |