|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Lever Shears |
| Dangers for humans and the environment |
|  | Risk of impact from unconfirmed hand lever Squeezing / separating fingers or hands when accessing the unclothed cutting line, by the movement of the stops, by the movement of the sheet. Noise from falling cuts |
| Protective measures and rules of conduct |
|  | Start work on the lever shears only after successful instruction and approval by the supervising teacher. Adjust the hold down to the material thickness. Only process the material thicknesses for which the cutting tools are designed. Transport and processing of metal sheets only with the appropriate means (Sheet metal transport clamps, protective gloves, safety shoes). The cutting line must be well lit and not covered. To combat noise, technical measures should be used, e.g. Use of slides that reduce the height of fall. | pE |
| Faults and dangers |
|  | In case of damage to the device: Shut down the device and inform responsible persons. In the event of breakage, jamming or other abnormalities, the lever scissors must not be used. Have the damage repaired by a specialist. |  |
| Accidents and First Aid |
|  | Keep Calm Involve first responders Emergency call: 144 Report accident and fill out accident report.Mehr anzeigen Weniger anzeigen |  |
| Tests – Maintenance - Disposal |
| Repairs: Repairs may only be arranged by the responsible teacher. A repair has to be documented. Maintenance: The maintenance intervals can be found in the manufacturer's operating instructions. A performed maintenance is to be documented. Disposal: After completing the shearing work, dispose of any leftovers in the marked collection container |
| Signatures |
| Supervisor: Signature: Town: Date: |  |