|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Magnetic stirrer with heating plate |
| Dangers for humans and the environment |
|  | The general rules and dangers for handling electrical equipment apply (see relevant operating instructions). (Dangers that are directly caused by the chemicals used are to be looked up in the respective safety data sheets or operating instructions for the chemical and method. Danger of burning on hot surfaces (hotplate may get over 300 ° C hot). Caution: Magnetism! Effects of the magnetic field are to be considered (pacemaker). Risk of electric shock. |
| Protective measures and rules of conduct |
|  | General information Eating, drinking or smoking is prohibited in all laboratory facilities! Personal protective measures | pE |
|  Put on protective clothing: lab coat, if necessary gloves and safety goggles  Remove warmed liquids with thermal gloves. Use • Before putting the device into operation, switch off the magnetic stirrer function (set the rotary speed control knob to the left-hand stop), do not start stirring until the stirrer with liquid and magnetic stirrer is already on the stirrer plate. Keep the mains cable away from the heating plate! Transport of the device only in the switched off and cooled state. |  |
| Faults and dangers |
|  | In the event of visible damage, do not operate the device. If faulty, unplug the power cord and inform the responsible manager. Repair and repair only by a specialist workshop Have customer service carried out. |  |
| Accidents and First Aid |
|  | First Aider: Pay attention to self - protection! If necessary, alert first responder, ambulance or doctor. Still burns for at least 10 minutes (running lukewarm water). If necessary, seek medical treatment. Inform the supervisor. |  |
| Tests – Maintenance - Disposal |
| Maintenance and repair work may only be carried out with the permission of the group leader. Have repaired and repaired exclusively by a specialist workshop / customer service. Disposal via old material collection points or specialist dealers. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |