|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Microwave |
| Dangers for humans and the environment |
|  | The general rules for handling electrical equipment apply (see relevant operating instructions). Danger due to microwave radiation. Risk of scalding from hot surfaces or steam. Risk of scalding due to bumping. Danger of bursting with closed containers. Danger due to heating of solvents - Solvents can be dissolved within seconds reach their boiling point! Fire hazard if excessive heating of solids (e.g., plastics) occurs. |
| Protective measures and rules of conduct |
|  | General information Eating, drinking or smoking is prohibited in all laboratory facilities! Personal protective measures | pE |
| Put on protective clothing: lab coat, disposable gloves, safety goggles Behavior rules Install microwaves vibration-free. Only use the microwave oven as intended. Only operate the microwave oven if the door seal is clean and undamaged - danger the emission of electromagnetic radiation! Use only suitable laboratory glassware and no closed containers. Do not introduce metal objects into the microwave Remove heated vessels from the microwave using a hot-hand or thermo-glove only. Observe the operating instructions of the manufacturer. Do not heat food in the microwave. Do not heat solvents or flammable substances in the microwave. Do not heat unknown substances in the microwave. Heat only small quantities in the microwave. Adjust heating capacity and duration to the substance to be heated Before using the microwave, inform yourself about it, whether when heating your substance Dangers can arise that you did not consider before. |  |
| Faults and dangers |
|  | In the event of visible damage, do not operate the device. Damage to the door is damaged if the door seals are damaged Electromagnetic radiation can not be ruled out, therefore a microwave oven is allowed not be used with damaged door seals. In the event of faults, pull out the mains plug and inform the responsible supervisor if possible. Repair and repair exclusively by a specialist workshop Have customer service carried out. |  |
| Accidents and First Aid |
|  | First Aider: Pay attention to self-protection! If necessary, alert first responder, ambulance or doctor. In case of burns / scalds, cool with water (at least 10 min.). Face and Do not leave the eyes burned. If necessary, arrange for medical treatment. Inform supervisors. |  |
| Tests – Maintenance - Disposal |
| Maintenance and repair work may only be carried out with the permission of the group leader be performed. Repair and repair only by a specialist workshop / customer service let carry out. Disposal via waste collection points or specialist dealers. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |