|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Milling Machine-Metall |
| Dangers for humans and the environment |
|  | Risk of injury if used improperly (especially for eyes and hands) Danger of catching by high-speed, rotating machine parts Risk of injury from flying chips, tools and parts Risk of skin damage and allergies when handling coolant Hearing damage due to noise Danger of electric current, especially in case of damage to electricity of leading line |
| Protective measures and rules of conduct |
|  | Before starting work, check that the machine is in a safe condition Firmly clamp the workpiece in the vice and remove the wrench Position protective devices in working position For tool change, measuring, cleaning etc. Switch off the machine Wear tight fitting clothes. Jewelry, e.g. Put down rings, chains, bracelets and watches. Secure longer hair with a hair tie, cap, or headscarf Wear safety glasses. Ear protection for noisy work Protective gloves are prohibited: danger of moving into the rotating parts Do not remove splinters, chips and waste by hand! Switch off the machine and use a chip hook, a hand brush or an approved industrial vacuum cleaner Wear tight fitting clothes Wearing gloves and jewelery is prohibited (Gloves only for material change, with secured, stationary machine) Use skin protection according to the operating instructions for cooling lubricant Safety shoes must be worn depending on the size of the workpieces Observe extended information for different turning techniques. | pE |
| Faults and dangers |
|  | In case of malfunction or damage to machinery or protective equipment Switch off the machine and secure against unauthorized restarting. Have damage repaired by qualified personnel only. |  |
| Accidents and First Aid |
|  | Switch off and secure the machine Inform first responders Provide immediate injury Emergency call: 144 |  |
| Tests – Maintenance - Disposal |
| Repair only by authorized and qualified persons For setup, maintenance and care work, disconnect or secure the machine from the mains After maintenance, the protective equipment must be checked Clean the machine after work Check the coolant regularly according to plan and replace if necessary (see Operating instructions for cooling lubricants) E-check every four years by a qualified electrician |
| Signatures |
| Supervisor: Signature: Town: Date: |  |