|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Milling Machine |
| Dangers for humans and the environment |
|  | Cutting injuries to the tool or chuck. Detecting clothing and hair by open drive or milling spindle. Danger of crushing by pull-in points. Injuries due to flying workpiece or tool parts or chips. High-speed and trailing drill. |
| Protective measures and rules of conduct |
|  | Operation of the machine only after instruction. Wear tight-fitting work clothing, safety shoes, and safety goggles! For long hair wear a hairnet or a suitable cap! Wearing jewelery (rings, chains, watches, visible piercings) is prohibited The wearing of gloves is prohibited. Attention to follow-up of the machine after switching off. Firmly clamp workpiece and tool, make sure that the machine vice is firmly seated. Do not touch the cutter at the cutting edge and remove the wrench. Perform tool and workpiece changes as well as measuring activities only when the machine is at a standstill. Do not use compressed air for cleaning Only remove chips with a chip hook, broom, brush or industrial vacuum cleaner. NEVER with bare hands. Modifications to the protective devices are prohibited. |  |
| Faults and dangers |
|  | In the event of faults, abnormalities of the machine, breakage and setting of tools, switch off the machine immediately, secure it against commissioning and inform the supervisor. Only eliminate faults at standstill. |  |
| Accidents and First Aid |
|  | Keep Calm Observe self-protection; Injured people recover, switch off the system Call first responder and, if necessary, emergency doctor. Emergency call: 144 Provide first aid Inform supervisors An accident report must be made in the case of accidents and near-misses |  |
| Tests – Maintenance - Disposal |
| The machine and the workplace are to be cleaned after use, tools and aids are to be put in the designated places. Repair and repair only by authorized and authorized persons. Observe the maintenance schedule of the manufacturer. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |