|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Oven with drying function |
| Dangers for humans and the environment |
|  | There are hazards due to: In the event of improper operation, safety and security measures may be taken. environmental hazards occur, e.g. if other than the expressly permitted products are filled. Risk of burns from touching hot surfaces, such as jars, materials, Risk of fire due to leaked or dropped hot material. Danger of scalding when extinguishing with water due to explosive formation of water vapor due to the usually very high temperatures. Danger of crushing fingers in the area of cover plates or, in the case of swiveling ovens, between oven and rack. |
| Protective measures and rules of conduct |
|  | Employees are to be made familiar with the operation of the stove, preferably by the manufacturer, before commissioning. Crucible furnaces may only be operated by technically suitable persons. Combustible material should be removed from the immediate vicinity of the stove (at least 800 mm). Never extinguish fires with water or foam. Only use materials whose properties and the like Melting temperatures are known. Operation with substances that may release explosive gases when warmed up is prohibited. Never use the oven without properly installed jars. Never use the oven to heat food. No intake of food or drink while working with the oven. Use suitable heat-resistant PPE to remove materials from the oven (protective gloves, apron, goggles) Regularly check the safety devices for proper function. Provide adequate and proper ventilation (away from the person) at the workplace. Place the stove on a fireproof floor; Furnish the oven environment fireproof. | pE |
| Faults and dangers |
|  | • Never use the stove with damaged or missing covers. Inform superiors. Only carry out troubleshooting by persons who have been trained to do so. are entitled. Always follow the manufacturer's instructions for troubleshooting. |  |
| Accidents and First Aid |
|  | In the event of burns, immediately cool affected areas with sufficiently cold water. Provide further 1.Aid as far as possible, if necessary visit doctor or call for help. Instruct emergency personnel and, if necessary, point out special risks. |  |
| Tests – Maintenance - Disposal |
| Cleaning the stove with water or non-flammable cleaning agents. Before maintenance a. Repair work Disconnect the heater from the power supply and secure against reclosing. Electrical cables u. Check safety covers regularly for integrity. Only carry out maintenance work by persons who are suitable for this purpose. Only carry out work on electrical equipment by a qualified electrician Work on hydraulic or gas technology. Only equip people with special knowledge and experience in this field. It is essential to observe the manufacturer's maintenance instructions. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |