|  | Operating instructions |  |
| --- | --- | --- |
| Technical Equipment – Devive – Machine - Tool |
| Shapers / ram planer |
| Environmetal and health Hazards |
|  | Flying chips, moving tools, etc. Detecting the hair, clothing, jewelery, etc. by means of drive, guide or tool Cutting, piercing, etc. on tool, workpiece, chips Intensive skin contact with cutting oil leads to the destruction of the acid mantle, degreasing, dehydration and irritation of the skin as a precursor of skin diseases. Even minor skin injuries, e.g. due to metal particles, increase the risk of a coolant-related skin disease |
| Safety Precautions |
|  | Check workstation for defects before starting work. Take skin protection measures if necessary. Cover long hair with a cap, hairnet or similar. Wear tight fitting work clothes with cuffs, roll up sleeves if necessary. Put down the wristwatch, finger rings, bracelets and loose necklaces, ties, scarves and more. Gloves must not be worn when bumping. Firmly clamp the chisel Wear safety glasses Do not endanger neighboring workplaces with flying chips or cutting oil (use protective device). Do not exceed the specified delivery. Clamp the workpiece firmly in the vice. To change workpieces, to measure, to clean, etc. Switch off the machine. Switch off the machine after use and secure it against unauthorized switching on. Remove chips only with a brush or hand brush. Änderung vorschlagenÜbersetzung teilen | pE |
| Malfunction and associated Risks |
|  | In case of damage or malfunction of the machine: Switch off and inform the instructor. Remove slipping hazards (eg due to chips or lubricants). Have the damage repaired by a specialist |  |
| First Aid |
|  | Switch off the machine. Inform first responders Take care of injured persons. Emergency call: 144 |  |
| Serving – Maintenance - Disposal |
| After completing the work, dispose of chips in the marked collection container. Clean the machine at the end of work. Clean up the machine environment at the end of work. Damage to the machine may only be eliminated by authorized persons. |
| Signatures |
| Group leader / Supervisor: Signature: Town: Date: |  |