|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Table and stand drill |
| Dangers for humans and the environment |
|  | Dangers due to cuts due to chips! Dangers due to handling of coolants and lubricants! Dangers of eyes and bodily injury due to worn material! Dangers due to noise! Dangers due to workpieces being spun around! Danger of hand injury due to sheep edged surfaces or the removal of material! Danger by detecting clothes or hair! Risk of foot injuries due to falling workpieces! |
| Protective measures and rules of conduct |
|  | behavior: The accident prevention regulations and the manufacturer's operating instructions must be observed! Check the machine for functionality before starting work! Clamp the workpiece and place it against the stop! Drill and workpiece change only when the machine is switched off! Remove chips with chip hooks or brooms! For long hair: wear hairnet or cap!! Tension and hold the workpiece properly during grinding Do not wear gloves when drilling! Do not wet the environment with coolant! Clean the machine after completing work and dispose of chips in the chip container |  |
| Faults and dangers |
|  | Switch off the machine immediately! Secure the machine against unintentional restart! |  |
| Accidents and First Aid |
|  | Carry out emergency measures at the scene of the accident Call ambulance / doctor Notify supervisors Emergency call: 144 |  |
| Tests – Maintenance - Disposal |
| Check the function and safety features of the machine before each use Cleaning and maintenance work only when the machine is switched off Observe the manufacturer's specifications regarding maintenance and care Have repairs carried out by qualified persons only |
| Signatures |
| Supervisor : Signature: Place: Date: |  |