|  | Operating instructions |  |
| --- | --- | --- |
| Work equipment – Equipment – Apparatus - Device |
| Ultrasonic cleaning compact unit |
| Dangers for humans and the environment |
|  | Risk of hearing loss during prolonged operation without hearing protection. Danger of burning when heating up the liquid. Danger from shattering glass. |
| Protective measures and rules of conduct |
|  | Personal protective measures Put on protective clothing (at least lab coat, disposable gloves, safety goggles). In case of continuous activity within 2 m of the ultrasonic cleaner, wear ear protection! Use Never operate the device without liquid! Distilled or deionized water without additives is not suitable for ultrasonic cleaning directly in the oscillating tank. Do not use flammable liquids or chemicals that contain or split off chloride ions for ultrasonic cleaning in the stainless steel pan. Use aggressive cleaning fluids (such as acids, saline solutions) only in service containers. Do not put anything on the bottom of the tub! Clean items to be cleaned in the appropriate hanging basket. Do not put in cleaning liquid during ultrasonic cleaning! During prolonged operation, the cleaning liquid heats up, therefore, when cleaning. Temperature-sensitive parts, check the temperature. When preheating the cleaning fluid at least every 30 min. the liquid stirred or 5 min. Ultrasound be switched on (Bumping!). Business: Make sure that the process is closed. Fill the oscillating tank with liquid up to the level mark. Connect the device to the mains. Operating Instructions Ultrasonic Bath, Page 2 of 2 Make sure that the items to be cleaned are completely covered with liquid. Turn the knob clockwise to the desired cleaning time, the green pilot lamp lights up. Reversing the rotation can shorten the cleaning time or switch off the device. For continuous operation, turn the knob all the way to the left (∞) and engage. To switch off,turn the knob to the right to "0" | pE |
| Faults and dangers |
|  | In the event of a fault, switch off the device immediately, disconnect the power plug and inform the supervisor. |  |
| Accidents and First Aid |
|  | If necessary, alert first responder, ambulance or doctor. superior inform (if necessary entry in the association book). |  |
| Thoroughly rinse and wipe the stainless steel tray. Do not use steel wool, scratches or scrapers. Have repairs carried out by authorized specialist personnel only. |
| Signatures |
| Supervisor: Signature: Town: Date: |  |